## Slide 1: HILTI Data Collection

## Slide 2: Objective
Work Load Detection
Anomaly Detection

## Slide 3: Sensors
A sensor is a device that is able to detect changes in an environment.
A sensor is able to measure a physical phenomenon (like temperature, pressure, and so on) and transform it into an electric signal

## Slide 4
Characteristics:
It should be sensitive to the phenomenon that it measures
It should not be sensitive to other physical phenomena
It should not modify the measured phenomenon during the measurement process

## Slide 5
Classification:
Passive sensors do not require an external power source to monitor an environment, while Active sensors require such a source in order to work.
Analog sensors produce an analog or continuous signal while digital sensors produce a discrete signal.

## Slide 6
Properties:
Range: The maximum and minimum values of the phenomenon that the sensor can measure.
Sensitivity: The minimum change of the measured parameter that causes a detectable change in output signal.
Resolution: The minimum change in the phenomenon that the sensor can detect.

## Slide 7: Types of sensors

## Slide 8: Sensors in a smart phone

## Slide 9: How to use Sensors in IoT
Two most popular boards used for prototyping are
Arduino Uno
    Microcontroller board based on an ATmega328P.
    Provides 6 analog and 14 digital pins.
    Can be used with analog and digital sensors.
Raspberry Pi
    Small “Single Board Computer” (SBC) based on Broadcom BCM2837B0
    Compatible with Operating Systems such as Linux, FreeBSD, NetBSD, OpenBSD, Plan 9, RiscOS and Windows 10 IoT Core
    Built in Camera, SenseHat (has lots of built-in sensors), Gertboard, Official Display

## Slide 10: Arduino

## Slide 11: Raspberry Pi

## Slide 12: How to measure Temperature and Humidity using Arduino
// Arduino IDE
#include "DHT.h"
#define PIN 8
#define DHTTYPE DHT11 // sensor type
DHT dht(PIN, DHTTYPE);
void setup()
{
Serial.begin(9600);
}
void loop()
{
int temp = dht.readTemperature();
int hum = dht.readHumidity();
Serial.println("Temperature: " + String(temp));
Serial.println("Humidity: " + String(hum));
delay(5000);
}

## Slide 13: How to use Movement Sensors with Raspberry Pi
//python code
import RPi.GPIO as GPIO
import time
GPIO.setmode(GPIO.BCM)
sensorPin = 7
GPIO.setup(sensorPin, GPIO.IN)
while True:
if GPIO.input(sensorPIN) == GPIO.LOW:
print "Motion detected"
else:
print "No motion"
time.sleep(0.5)

## Slide 14: Actuator
An actuator is a mechanism for turning energy into motion
Actuators can be categorized by the energy source they require to generate motion

## Slide 15: How Sensors and Actuators interact with the physical world

## Slide 16: Smart object

## Slide 17
Ultrasonic Sensor
Temperature Sensor
Vibration Sensor
Accelerometer Sensor

## Slide 18: Sample Dataset

## Slide 19: Sample arduino code